1708E - 8-Bits Processor Simulator
Design & Architecture
Revision 1

Yanick Poirier
May 2017
# Registers
This section describes all the registers contained in the processor. There is a total of nine (16) registers available for use, some may be read-only, write-only or, almost all of them, read and write registers.
Registers are identified as follow:
Name	Mnemonic	Size	Code
Working Register 0	R0	8	0000
Working Register 1	R1	8	0001
Working Register 2	R2	8	0010
Working Register 3	R3	8	0011
Working Register 4	R4	8	0100
Working Register 5	R5	8	0101
Working Register 6	R6	8	0110
Working Register 7	R7	8	0111
Address Register 0	ADDR0	16	1000
Address Register 1	ADDR1	16	1010
Status Register	SR	8	1110
Stack Pointer	SP	8	1111
Instruction Register	IR	8	Not required
Instruction Pointer	IP	16	1100
Instruction Counter	IC	4	Not required
Tick Register	TR	56	Not required

## Working Registers
## The Working registers (Rx) are general purpose register used for manipulating almost any kind of information. There is a total of 8 working registers named R0 through R7. Each register contains 8-bits of data.
## Address Register
## This processor has two 16-bits address registers (ADDR0 and ADDR1). Each ADDR is composed of two 8-bits registers for a total of 65536 (64K) memory addresses. The high address byte is stored in register ADDRxH and the low address byte is stored in ADDRxL, where x is the address register number. This means the all memory addresses within the selected bank can be noted as ADDR0 (or ADDR1) as well as ADD0H:ADDR0L (or ADDR1H:ADDR0L).
Bit 7-0
R/W

Bit 0-7: Data
Data being processed

## Status Register
The Status register (SR) is usually set by the ALU module to notify or module of the outcome of an arithmetic or logic operation. The SR is an 8-bits register describe in the following table.
Bit 5-7	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0
R-0	R/W	R/W	R-0	R/W	R/W

Bit 5-7: Not Used
Read as 0.

Bit 4: Parity (P)
After arithmetic or logic operation, if result has even number of 1s, the flag is set. If it has odd number of 1s, flag is reset.

Bit 3: Digit Carry (DC)
In arithmetic operation, when carry is generated by digit D3 and passed on to digit D4, the DC flag is set. This flag is used only internally for BCD operation.

Bit 2: Not Used
Read as 0.

Bit 1: Zero flag (Z)
The zero flag is set if ALU operation result is 0.

Bit 0: Carry flag (C)
If arithmetic operation result is in a carry, the carry flag is set, otherwise it is reset.
## Stack Pointer Register
## The Stack Pointer register (SP) is an internal 8-bits address register that is used the temporarily preserve information (stack). Data stored on the stack is accessed using a LIFO (Last-In, First-Out) mechanism. The content of this register cannot be directly written to. The SP register is managed internally.
## Instruction Register
## The Instruction register is a 19-bit register that contains the instruction be processed.
## Instruction Pointer
## The Instruction Pointer register is a 16-bit register that contains the address in memory of the next instruction to load. The high byte portion is referred as IPH while the low byte portion is called IPL
## Instruction Counter
## The Instruction Counter register is 4-bits register that counts the clock cycles during the execution of an instruction. The counter is reset automatically when the instruction terminates.
## Tick Register
## The Tick register is a 56-bits read-only register that counts the number of clock pulse that occurred since the processor has started-up.
# Instruction Set
This section describe the instruction set for this processor.
Data operations
1. LDA reg, x (Load Data at Address pointed in ADDRx into register reg)
2. MOV dest,src (MOVe data from register src to register dest)
3. MOVK reg,val (Move a literal value val in reg)
4. SDA reg, x (Store Data in register reg at Address pointed in ADDRx)
5. SWAP reg1,reg2 (Swap the content of reg1 and reg2).
Bit operations
1. LSL reg (Shifts the bits in the register reg 1 bit to the left).
2. LSR reg (Shifts the bits in the register reg 1 bit to the right).
3. RBC reg,b (Clear the bit b in register reg)
4. RBS reg,b (Set the bit b in register reg)
5. RLC reg (Rotates the bits in the register reg 1 bit to the left using the carry bit).
6. ROL reg (Rotates the bits in the register reg 1 bit to the left).
7. ROR reg (Rotates the bits in the register reg 1 bit to the right).
8. RRC reg (Rotates the bits in the register reg 1 bit to the right using the carry bit).
Arithmetic operations
1. ADD reg1,reg2 (Adds the content of register reg2 to register reg1 and store the result back in register reg1).
2. ADDK reg,k (Adds the constant k to register reg1 and store the result back in register reg1).
3. ALS reg (Shifts the bits in the register reg 1 bit to the left carrying the D7 bit with it).
4. DEC reg (Subtract 1 from the value in reg and store the result back in reg)
5. INC reg (Add 1 to the value in reg and store the result back in reg)
6. SUB reg1,reg2 (Subtract the content of register reg2 from register reg1 and store the result back in register reg1).
7. SUBK reg,k (Subtract the constant k from register reg1 and store the result back in register reg1).
Logic operations
1. AND reg1,reg2 (Performs a logical AND operation between registers reg1 and reg2 and put the result back in register reg1).
2. ANDK reg,k (Performs a logical AND operation between the register reg and the constant k and put the result back in register reg).
3. NOT reg (Performs a logical NOT operation (1s complement) on register reg and put the result back in register reg).
4. OR reg1,reg2 (Performs a logical OR operation between registers reg1 and reg2 and put the result back in register reg1).
5. OKK reg,k (Performs a logical OR operation between the register reg and the constant k and put the result back in register reg).
6. XOR reg1,reg2 (Performs a logical XOR operation between registers reg1 and reg2 and put the result back in register reg1).
7. XORK reg,k (Performs a logical XOR operation between the register reg and the constant k and put the result back in register reg).
Conditional operations
1. JA addr (Jump at the specified address if the Alternate Carry flag is set)
2. JC addr (Jump at the specified address if the Carry flag is set)
3. JNA addr (Jump at the specified address if the Alternate Carry flag is clear)
4. JNC addr (Jump at the specified address if the Carry flag is clear)
5. JNP addr (Jump at the specified address if the Parity flag is clear)
6. JNS addr (Jump at the specified address if the Sign flag is clear)
7. JNZ addr (Jump at the specified address if the Zero flag is clear)
8. JP addr (Jump at the specified address if the Parity flag is set)
9. JS addr (Jump at the specified address if the Sign flag is set)
10. JZ addr (Jump at the specified address if the Zero flag is set)
11. SBC reg, b (Skip the next instruction if the bit b in register reg is cleared)
12. SBS reg,b (Skip the next instruction if the bit b in register reg is set)
Others
1. NOP (No Operation)
2. JMP addr (Unconditional jump to the specified address)
3. RTC (Reads the Tick Register and put the result in the working registers
4. RTCB reg,byte (Reads the specified byte value from the tick register and stores it in reg).
# Instruction Processing
This section describes how the instruction are being process and determine how many clock pulses are required for each instruction.
Mnemonic		Description	Clock Pulse	16-bits Opcode	Status flags affected	Notes
Data oriented operations
ADD	d, s	Add the content of register s to register d (d = d + s)		0010 10dd ddds ssss	C, Z
ADDB	r,k	Add the literal k to register d (d = d + k)		010k kkkk kkkr rrrr	C, Z
ADDBC	r,k	Add the literal k and the carry bit to register d (d = d + k + C)		010k kkkk kkkr rrrr	C, Z

MOV	d, s	Move content of register s to register d		0010 01dd ddds ssss	Z
MOVB	r,k	Move the 8-bit literal k to register r		010k kkkk kkkr rrrr	Z
SWAP	d, s	Swap the content of register d with register s		0010 00dd ddds ssss

Instruction	Bit 15	Bit 14	Bit 13	Bit 12	Bit 11	Bit 10	Bit 9	Bit 8	Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0
NOP	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
RST	0	0	0	0	0	0	0	0	0	0	0	0	1	x	x	0
RTC	0	0	0	0	0	0	0	0	0	0	0	0	1	x	x	1

SMB k	0	0	0	0	0	0	0	0	0	0	0	1	0	0	k	k

NOT r	0	0	0	0	0	0	0	1	0	0	0	R	R	R	R	R
RTCB r	0	0	0	0	0	0	0	1	0	0	1	R	R	R	R	R
ALS r	0	0	0	0	0	0	0	1	0	1	0	R	R	R	R	R
RLC r	0	0	0	0	0	0	0	1	0	1	1	R	R	R	R	R
RRC r	0	0	0	0	0	0	0	1	1	0	0	R	R	R	R	R
ROL r	0	0	0	0	0	0	0	1	1	0	1	R	R	R	R	R
ROR r	0	0	0	0	0	0	0	1	1	1	0	R	R	R	R	R
LSL r	0	0	0	0	0	0	0	1	1	1	1	R	R	R	R	R
LSR r	0	0	0	0	0	0	0	1	0	0	0	R	R	R	R	R
INC r	0	0	0	0	0	0	0	1	0	0	1	R	R	R	R	R
DEC r	0	0	0	0	0	0	0	1	1	1	0	R	R	R	R	R

LDA r, n	0	0	0	0	0	0	1	0	0	0	R	R	R	R	R	N
SDA r, n	0	0	0	0	0	0	1	0	0	1	R	R	R	R	R	N
LDAI r	0	0	0	0	0	0	1	1	0	0	R	R	R	R	R	x
SDAI r	0	0	0	0	0	0	1	1	0	1	R	R	R	R	R	x
LDAD r	0	0	0	0	0	0	1	1	1	0	R	R	R	R	R	x
SDAD r	0	0	0	0	0	0	1	1	1	1	R	R	R	R	R	x

RBC r,b	0	0	0	0	1	0	0	0	R	R	R	R	R	B	B	B
RBS r,b	0	0	0	0	1	0	0	1	R	R	R	R	R	B	B	B
SBC r, b	0	0	0	0	1	0	1	0	R	R	R	R	R	B	B	B
SBS r,b	0	0	0	0	1	0	1	1	R	R	R	R	R	B	B	B
BTSS r, b	0	0	0	0	1	1	0	0	R	R	R	R	R	B	B	B
BTSC r, b	0	0	0	0	1	1	0	1	R	R	R	R	R	B	B	B

SWAP d, s	0	0	1	0	0	0	D	D	D	D	D	S	S	S	S	S
MOV d,s	0	0	1	0	0	1	D	D	D	D	D	S	S	S	S	S
ADD d, s	0	0	1	0	1	0	D	D	D	D	D	S	S	S	S	S
SUB d,s	0	0	1	0	1	1	D	D	D	D	D	S	S	S	S	S
AND d,s	0	0	1	1	0	0	D	D	D	D	D	S	S	S	S	S
OR d,s	0	0	1	1	0	1	D	D	D	D	D	S	S	S	S	S
XOR d, s	0	0	1	1	1	0	D	D	D	D	D	S	S	S	S	S

MOV r, k	0	1	0	R	R	R	R	R	K	K	K	K	K	K	K	K
ADDK r, k	0	1	0	R	R	R	R	R	K	K	K	K	K	K	K	K
SUBK r, k	0	1	1	R	R	R	R	R	K	K	K	K	K	K	K	K
ANDK r, k	0	1	1	R	R	R	R	R	K	K	K	K	K	K	K	K
ORK r,k	0	1	0	R	R	R	R	R	K	K	K	K	K	K	K	K
NOTK r,k	0	1	0	R	R	R	R	R	K	K	K	K	K	K	K	K
XORK r,k	0	1	1	R	R	R	R	R	K	K	K	K	K	K	K	K

JMP a	1	0	A	A	A	A	A	A	A	A	A	A	A	A	A	A
Opcode: 6-bits
Register 1: 5-bits
Register 2: 5-bits
Constant : 8 bits
Address : 8 bits
## Common Processing
Each instruction processing must go through a common path in order for the instruction to be decoded. So even before the instruction is executed, it must be loaded and decoded first.
1. Put IPH to bits 8-15 on the address bus.
2. Put IPL to bits 0-7 on the address bus.
3. Put memory content at IPH:IPL into IRH
4. Increment IPL
5. Put memory content at IPH:IPL into IRL